## Slide 1: Advanced Control of Robotic Surface Treatments
RPI: John Wen, Glenn Saunders, William Lawler, Shuyang Chen, Alex Elias
UTRC: Abhijit Chakraborty, Mike Klecka
07/18/2019

## Slide 2
Agenda (CII 8003)
  10:30-11:00 Introduction
  11:00-11:30 Project motivation, UTRC needs
  11:30-12:00 Project Overview (objective, team, duration, management)
  12:00-1:00 Lunch
  1:00-2:00 Technical Overview (goals, approach, milestones, status)
  2:00-2:30 Programmatic Overview (reporting, cost share, reviews)
  2:30-3:00 Tour (CII highbay, CII 8218)

## Slide 3
Project Motivation
Deep rolling:
workpiece surface exposed to high local mechanical load using a spherical or cylindrical type tool to induce work hardening and compressive residual stress
Altering mechanical behavior of material, enhancing stability of near-surface structure, improving peak-to-peak value of surface roughness.
Robotic roller burnishing
Compared with CNC: lower cost, higher throughput, process flexibility for parts
Large industrial robots: heavy loads, while eliminating work-envelope and motion constraints: hard-to-reach spots like corners, square-bottomed areas, and complex curvatures.
Smooth transition of forces around different geometries or segments of the part: challenging for CNC machines

## Slide 4
Project Overview
Objective: Apply, demonstrate, and evaluate compliance force control and iterative learning control (ILC) for deep rolling or burnishing processes using an industrial robot equipped with a roller end effector and force/torque sensor.
Project Team:
UTRC: Abhijit Chakraborty, Mike Klecka
RPI: John Wen, Glenn Saunders, William Lawler, Shuyang Chen, Alex Elias
Project Duration: 12 months (5/1/19-4/30/20)
Management: Project meetings (bi-weekly?) Project repository (box? GitHub?) Monthly/quarterly report? ARM interface?

## Slide 5
Technical Overview
Task 1: Requirement Development
- Fatigue life requirement
- Robot accuracy requirement
Task 2: Motion and Force control for Deep Rolling
- Co-simulation development: ABB RobotStudio + UTRC FEA
- Hybrid motion/force control algorithm development
- Iterative refinement: ILC
Task 3: Development of Closed-Loop Robotic Deep Rolling Cell
- RPI Testbed
- UTRC Testbed
Task 4: Experimental Tests and Evaluations
- Baseline case studies
- Closed loop case studies
Task 5: Project Evaluation: KPPs

## Slide 6
Approach
Testbed design (size/geometry of coupon, range of force, coupon fixturing, post-mortem assessment)
Control architecture (EGM? ROS?)
State machine
  Part geometry identification
  Path planning for coverage (part of the project, or any path coverage?)
  Force set point specification
  Motion generation based on curvature
  Assessment (based on F/T or material properties/uniformity as well?)
  Update motion plan and repeat 4-5.

## Slide 7
Performance Metrics and KPP
Metrics:
Normal force: average and stdev of normal force error
Robot tool path: average and stdev of path tracking error
Product quality: surface deformation, fatigue life
Cycle time
Baseline: Existing UTRC off-line toolpath generation
Post-treatment verification: microstructure characterization (surface roughness, deformation, residue stress), fatigue tests

## Slide 8
Key Performance Parameters (KPPs)

## Slide 9
Milestones

## Slide 10
Programmatic Overview
ARM project management: Cara
ARM project kick off: next Tuesday
Tracking cost share and spending: RPI will wait for UTRC
Reporting: 15th of every month. RPI will provide input several days before
Reviews: quarterly review with ARM, mid-year review (ARM TAC call in: Nov 2019)

## Slide 11
Action Items
Finalize RPI subcontract – anything else needed from RPI? (wait for UTRC)
Sharable copy of the proposal (Abhijit)
Set up project repository (GitHub: William)
Set up meeting schedules (Whenisgood: John)

## Slide 12
Lab Tour
CII Highbay
  ARM Composites Assembly Quick Start Project
  Robot welding cell
  MPS space (briefly)
CII 8218
  NASA Satellite Servicing
  Assistive Robot
  Baxter-on-Wheels
  Kinova-on-Omni-Base